## Slide 1: surf
Lexie
2026.1.23

## Slide 2: Inputs and outputs
Input: [X_species (9), rho/rho0, T/T0, log(dt)] → 12 features
for the time, log scale would be better, because time scales change a lot and if not the neural network would not be able to predict super tiny changes. The same applies for concentrations, they should be in log scale, because the tiny changes if not are not going to be appreciated by the NN. In general, it is known that setting inputs so that they are all of the same order of magnitude works better.
Output: [X_species (9), rho/rho0, T/T0] → 11 features
You could use a reference pressure an temperature to non-dimensionalize the inputs. For example, give the network, T/T0 and P/P0, where 0 values are standard values at atmospheric conditions. T0 = 293K and P0 = 1atm. Also it might work better if you put inputs in log scale, log(T/T0) and log(P/P0). You can try the two variants.

## Slide 3: Species
Molar fractions of species. Xi = ni/N
Specify mixture state, P = (n*W/V) * (R/W) * T: two parameters. rho = (n*W/V), Rg = (R/W). P = rho * Rg * T. Two parameters: rho, T.

## Slide 4: Governing equations
Constant mass: conservation of number of atoms. As many equations as different type of atoms.
Constant volume, constant energy.